Simple work flow for APES8.41

1. (Optional)Recompile from the source code:
a. With Intel compiler and the CPU that support AVX512:
Simply run:
make
b. With the Intel Compiler and the CPU only support AVX2:
make -f makefileAVX2
c. To make with gcc/g++:
make -f makegcc
If the gsl library is missing, here is how I got one installed on Ubuntu:
sudo apt-get install libgsl-dev
The ‘make’ will generate different executable with corresponding names: APES, APESAVX2 and APESGCC. They all read the input file called ‘input.txt’.

2. The parameters in the ‘input.txt’ file are listed below.
"type" indicate the type of the particle, "0" means proton, "1" means electron, "2" means Au;
"csv_out" control the output of csv file;
"dynamicOn" control the behavior of the beam dynamic at the beginning of the time, default is “off”;
“turn_start” legacy parameters, starting number of the turn, just set it to “0”;
“mainRF” the index of the RF used by the code to calculate ramping of Vref and Iref;
“main_detune” the index of RF used by the code to calculate ramping of the detuning;
“R”, the radius of the ring;
“GMTSQ”, the gammaT^2;
“Gamma”, the reference gamma of the beam;
“nBeam”, the number of beams;
“beam_shift”, the shift between two beams in unit of mainRF cycle;

“n_turns”, total number of turns the code with run;
“n_dynamicOn”, the number of turn we turn on the beam dynamics;
“n_bunches”, the number of bunches in one beam;
“n_fill”, the turn we start to ramp the bunches charge;
“n_q_ramp”, the number of turns it takes to ramp the charge;
“n_detune_start”, the turn we start to ramp the detuning;
“n_detune_ramp”, the legacy parameter, not real in use;
“n_detune_ramp_tot”, the turn we finish the ramping of the detuning;
“n_I_ramp_start”, the turn we start to ramp the driving current of the RF amplifier;
“n_I_ramp_end”, the turn we finish ramping the driving current of the RF amplifier;

“Prad”, the radiation power of the beam, in unit of watts. We need to compensate it with the RF voltage;
“t_rad_long”, the longitudinal radiation damping time, in unit of seconds;
“Ek_damp”, the artificial damping on the bunch energy before the bunch is rampped to full charge, in unit of number of synchrotron oscillation;
“Ek_damp_always”, the artificial damping on the bunch energy after the bunch is rampped to full charge, in unit of number of synchrotron oscillation;
“Npar”, number of macro particles in one bunch;
“NperBunch”, the nubmer of real particles in one bunch;
“N_bins”, the number of time slices per RF cycle;
“fill_step”, the number of RF cycles between bunches;
“siglong”, the sigma gamma;
“A”, the 95% particle emittance, assuming Gaussian bunch;

“nRF”, number of RF systems;
“nRF1”, number of RF systems in ring 1;
“nRFc”, number of RF systems shared by both rings;
“nRF2”, number of RF systems in ring 2;
“nHOM”, legacy parameters, not in use;

“nCav”, array type parameters, indicate the number of cavities for each RF system, length of the array should be equal to “nRF”;
“h”, array type parameters, the harmonic numbers of each RF systems;
“RoQ”, array type parameters, the R over Q of each RF systems, circuit definition;
“I_Q_ref_ini”, array type parameters, the initial values of the the Q component of the reference driving current;
“I_Q_ref_final”, array type parameters, the final values of the the Q component of the reference driving current;
“I_I_ref_ini”, array type parameters, the initial values of the the I component of the reference driving current;
“I_I_ref_final”, array type parameters, the final values of the the I component of the reference driving current;
“Iref_I”, array type parameters, the values of the the I component of the reference driving current, should be equal to “I_I_ref_final”;
“Iref_Q”, array type parameters, the values of the the Q component of the reference driving current, should be equal to “I_Q_ref_final”;
“Vref_I”, array type parameters, the I component of the reference cavity voltage;
“Vref_Q”, array type parameters, the Q component of the reference cavity voltage;
“detune”, the initial detune of each RF system, in unit of Hz;
“detune_ini”, the initial detune of each RF system;
“detune_mid”, legacy parameter, the mid point of the detune;
“detune_final”, legacy parameter, the final value of the detune of each RF system;

“delay”, array type parameters, the delay for each direct feedback system, not really properly implemented yet;
“n_fb_on”, array type parameters, the turn we turn on the direct feedback;
“gII” to “gQIi”, the gains of the direct feedback, the integral part is not implemented;
“PA_cap”, the cap of the power amplifier, not implemented;
“epsilon_comb”, the epsilon of the comb filter;
“g_comb”, the g number of the comb filter;
“QL”, loaded Q of each RF system;

“n_ini_CBI”, the number of coupled bunch modes to initialize;
“mu”, the mus of the coupled bunch mode;
“CBI_ini_amp”, the amplitudes of the coupled bunch modes, in unit of gamma;

Practically it is more convenient to run the code from a python script that can dispatch jobs with different parameters. We provided several example script for different type of job. These scripts are by no means the most sophisticated but to show the basic function of the code.

3. Example script to run the job:
“example_5SOM.py”: